## Slide 1: Chapter 1 Introduction: Local energy communities ?

## Slide 2: Why local energy communities (in our opinion) ?

## Slide 3
To be consistent with the energy transition: sufficiency, efficiency, renewables [1-4].
Yes but not only.
Renewables: e.g., solar panels
Efficiency: e.g., building insulation
Sufficiency: e.g., lower thermostat
[1] “RTE : Futurs énergétiques 2050”
[2] “ADEME : Transition(s) 2050”
[3] “Shift Project : le plan de transformation de l'économie française”
[4] “NégaWatt : Scénario 2022”
Proximité retrouvée
Trade-off ?
Leopold Kohr, Ivan Illich, Gilbert Simondon, Bruno Latour.

## Slide 4: What are local energy communities (in our opinion) ?

## Slide 5
Energy communities is a flexible concept [1] — i.e., our definition not absolute.
Two ingredients: geographic scope & temporal scope.
“A governance with the participation and effective control of local members whose primary economic activity is not the energy sector,
A primary purpose aimed at generating social and environmental benefits rather than a focus on financial profits.” [2]
[1] Brummer, ‘Community Energy – Benefits and Barriers’.
[2] Lowitzsch, Hoicka, and van Tulder, ‘Renewable Energy Communities under the 2019 European Clean Energy Package – Governance Model for the Energy Clusters of the Future?’

## Slide 6
[1] Jarra Hicks and Nicola Ison. « An Exploration of the Boundaries of ‘Community’ in Community Renewable Energy Projects: Navigating between Motivations and Context ». In: Energy Policy 113 (Feb. 2018), pp. 523–534. doi: 10.1016/j.enpol.2017.10.031

## Slide 7
Power [kW]
Morning
Noon
Evening
Surplus
Grid consumption
Local consumption
Consumption
Production
Self-consumption (see chapter 2):

## Slide 8
In France:
Producers
Consumers
Organizing Legal Entity
Billing
Metering data
Sharing « keys »
Distribution System Operator
Energy
supplier
1 km radius
Electrical grid
…
…
…
30 minutes
1 km radius
Sharing keys:
Static
Dynamic default
Dynamic
Notes: Objet social (communauté d’hommes et de femmes)
On utilise le réseau d’électricité publique (pas d’autarcie)
Chaque consommateur garde un fournisseur extérieur pour couvrir le complément d’électricité
Notion de prise de décision collective sur la répartition du productible.
Couche physique et couche contractuelle

## Slide 9
In August 2021, the regulated price of electricity is 9.74 cent€/kWh before taxes [16], and includes 3.71 cent€/kWh for network fees (TURPE) which means that producers can expect to sell electricity at about 6 cent€/kWh.
With the 2022 regulated price, and if we remove 3.71 cent€/kWh for grid fees, this leaves a potential value of 10 cent€/kWh for producers selling within a community,
If consumers are willing to accept a larger TURPE in the winter, solar power could be sold at about 13 cent€/kWh with a 0.73 cent€/kWh TURPE and still fall below the regulated electricity price.
[PV + battery LCOE] This would enable a price of electricity at 20 cent€/kWh plus 3.71 cent€/kWh and 3.2 cent€/kWh in TURPE and local taxes and a 20 % VAT for a total cost after tax of 32.3 cent€/kWh.
Whether local energy communities can extend on the public grid or not, is a major difference between national implementations in Europe.

## Slide 10: Research landscape and questions.

## Slide 11
Research question #1:
How to coordinate local consumption with production within a community?

## Slide 12
Research question #2:
Is more renewable energy systems always better for local energy communities?

## Slide 13: Chapter 2 What does it means to “self-consume” ?

## Slide 14
Distribution grid
Meter #1
Meter #2
Demand
Production
Feed-in-tariff
Distribution grid
Meter #1
Demand
Production
Self-consumption
Notes: Différence physique limité (compteurs)
Différence économique et « philosophique » marquées

## Slide 15
Power [kW]
Morning
Noon
Evening
Surplus
Grid consumption
Local consumption
Consumption
Production
Self-consumption =
+
Self-sufficiency =
+

## Slide 16: What’s the impact of time intervals ?

## Slide 17
With 30 min intervals:
self-sufficiency = 100%
10 AM
10:30 AM
With 15 min intervals:
self-sufficiency = 50%
…
…
load(t)
prod(t)

## Slide 18
00:00
Jun 1, 2014
12:00
00:00
Jun 2, 2014
12:00
00:00
Jun 3, 2014
12:00
00:00
Jun 4, 2014
0
1
2
3
4
5
6
Power [kW]
Solar production
Load profile

## Slide 19
0
1
2
3
4
5
0
10
20
30
40
50
60
70
80
90
PV size [kWp]
Self-sufficiency [%]
5 min
15 min
30 min
60 min
1 day
1 week
1 month
1 year
Diurnal
value gap
(31%)
Seasonal
value gap
(26%)
Weekly
value gap
(5%)

## Slide 20: How to include storage ?

## Slide 21
00:00
06:00
12:00
18:00
-2
-1
0
1
2
3
00:00
06:00
12:00
18:00
-1
0
1
2
3
4
Power [kW]
+
a) Storage = production
00:00
06:00
12:00
18:00
-1
0
1
2
3
4
00:00
06:00
12:00
18:00
-1
0
1
2
3
4
b) Storage = production & demand
Power [kW]
Storage
Production
Consumption
Self-sufficiency
Self-sufficiency
Notes: Storage = demand
SS = 12 / 21 = 57%

## Slide 22
00:00
Jun 2, 2014
03:00
06:00
09:00
12:00
15:00
18:00
21:00
−3
−2
−1
0
1
2
3
4
5
Household power [kW]
−10
−5
0
5
10
15
20
25
30
35
40
45
Self-sufficiency [%]
Metrics
Battery profile
Solar production
Load profile
No storage
Definition 2
Definition 1

## Slide 23
00:00
Jun 2, 2014
03:00
06:00
09:00
12:00
15:00
18:00
21:00
0
1
2
3
4
5
Household power [kW]
0
0.5
1
1.5
2
2.5
0
10
20
30
40
50
60
70
80
PV size [kWp]
Self-sufficiency [%]
Battery profile
Solar production
Load profile
(35%) Definition 2
(33%) Net-metering
(31%) Definition 1

## Slide 24: Do we need storage to “self-consume” ?

## Slide 25
00:00
May 1, 2019
12:00
00:00
May 2, 2019
12:00
00:00
May 3, 2019
12:00
00:00
May 4, 2019
12:00
00:00
May 5, 2019
0
10
20
30
40
50
60
Power [kW]
Solar production
Load profile

## Slide 26
00:00
May 1, 2019
06:00
12:00
18:00
00:00
May 2, 2019
06:00
12:00
18:00
00:00
May 3, 2019
−20
−10
0
10
20
30
40
50
60
Power [kW] — SOC [kWh]
Solar production
Load profile
Battery power profile
Battery SOC

## Slide 27
0
1
2
3
4
5
0
10
20
30
40
50
60
70
80
90
100
PV size [kWp/household]
Self-sufficiency [%]
2 kWh
4 kWh
6 kWh
8 kWh
No storage
1 day
1 year
B
C
A
1.5
10%
10%

## Slide 28: What is the impact of load on self-sufficiency ?

## Slide 29
0
1
2
3
4
5
0
10
20
30
40
50
60
70
80
90
100
PV size [kWp/household]
Self-sufficiency [%]
Self-consumption
Self-sufficiency
Natural
self-sufficiency
1 year

## Slide 30
00:00
Jun 11, 2019
03:00
06:00
09:00
12:00
15:00
18:00
21:00
0
5
10
15
20
25
30
35
Power [kW]
Solar production
10% NSS
90% NSS
42% NSS

## Slide 31
0.5
1
1.5
2
2.5
3
3.5
4
4.5
0
10
20
30
40
50
60
70
80
90
100
PV size [kWp/household]
Self-sufficiency [%]
1 year
10% NSS
20% NSS
30% NSS
40% NSS
50% NSS
60% NSS
70% NSS
80% NSS
90% NSS
Original data
NSS = 35.5%

## Slide 32: Chapter 3 How to coordinate self-consumption within communities?
Notes: Historical narrative (see ”quoi de neuf” avoid the innovative narrative)
What level of complexity do we expect our communities ?
Not just a question of physical coordination

## Slide 33: What do we mean by coordination?

## Slide 34: What is the expected complexity of local energy communities ?

## Slide 35
What is the expected complexity of local energy communities (at each scale)?
[1] Siegenfeld and Bar-Yam, ‘An Introduction to Complex Systems Science and Its Applications’.
Coordination actions to maximize revenues
Community #1
« less complex »
Community #2
« more complex »
« Individual » actions
« Collective » actions
« Temporal » actions
« Spatial » actions
…
« Individual » actions
Grid
Grid
DSO
1
1
1
1
2, 3, 4
Notes: More or less complex energy communities (with different scales involved, coherent or corrolated)
Coordination with more actions can be necessary but never sufficient for better performance (good action)
Unforeseen evolution of communities, how to design an evolutionary coordination (keep good mutations)?

## Slide 36
Non-exhaustive list of expectations:
  Individuals with multiple :
    batteries,
    but also shapeable loads,
    and deferrable loads,
    or nothing;
  Maximize revenues for all individuals considering :
    individual time of use pricings,
    fees from the DSO for power exchanges,
    cost of equipment ageing,
    cost of lost of comfort;
  Multiple participants (residential, commercial building, office buildings, …) within a 2km diameter;
  Individuals with production units or not;
  Resources directly own by the community;
  Keep individual load profiles secured and private;
  Communities rapidly changing size with on-boarding and off-boarding of individuals;
  Interface with individual members to support behavioural nudges;
  Ensure that grid constraints are not violated;
  Provide some interface for grid services with the DSO, and TSO levels.
Notes: Non exhaustive list some expectations, we dont’ prioritize last 4 for reasons that we can discuss later
Coordination strategies themselve form complex systems (i.e., many actions interact with each others)

## Slide 37: What “eco-system” around coordination strategies ?

## Slide 38
Physical
coordination
Social coordination
(governance)
Economical coordination
Defining fairness
Revenues
Defining strategy
Environment
(regulatory, physical)
[1] Mengelkamp et al., ‘Designing Microgrid Energy Markets’.
[2] Cox, Arnold, and Villamayor Tomás, ‘A Review of Design Principles for Community-Based Natural Resource Management’.
Not only physical coordination.

## Slide 39
Costs allocation has some degrees of freedom with physical flux:
Physically at 12:15 pm
Economically at 12:15 pm
kWh
The price is another adjustment variable.
prod. #1
cons. #3
cons. #2
1
2
3
kWh
1
2
3
Pro rata of total consumption
Prioritization of cons. #2
0.66
1.33
1.0
1.0
2
3
share #2 = 33% of 2kWh
share #3 = 66% of 2kWh
share #2 = 1kWh
share #3 = 2kWh - 1kWh
Production
Consumption
[1] Diva et al., ‘’.
Notes: Not only is possible to do without (expected from passive communities)
The economical dispatch has some degree of freedom with regard to physical flux
Physically use all resources « together » and still economically « reward » resource owners (increase the cake size, and still share it how we want).

## Slide 40
Prod. 1
1 | … | 0
… | … | …
0.75 | … | 0.1
Prod. n
…
Cons. 1
Cons. n
…
Time
=100%
=100%
=100%
12:15 pm
12:30 pm
1:00 pm
…
Sharing keys:

## Slide 41: A review of coordination strategies
Centralized / Decentralized
Individualist / Collaborative
Notes: Expected complexity we want to reach at each scale (house, community, inter-communities, national)
Physical coordination depends on cost allocation and human organization
Cost allocation can provide a level of abstraction from physical flux (to some extend)
2 axes of review for coordination strategies.

## Slide 42: Decentralized versus centralized ?

## Slide 43
Centralized / Decentralized
Classification based on communication capabilities between devices and a platform (i.e., 1-way or 2-way), and whether local decisions are taken locally or not [1].
[1] Kok and Widergren, ‘A Society of Devices’ (smart energy management matrix).
Notes: ICT = communication (blockchain, virtual machines on a server (agent), central influx, MQTT)
Control = algorithm = ADMM or central optimization or PID, …
Power system = central battery or many small batteries ? Physical distribution of resources
For 3 batteries centralized controller will be more efficient, for 1 million…
Centralized system choosen by a distributed governance ? Is it still distributed ?

## Slide 44
#1
#3
#2
Local control
#1
#2
Local control
Communication

## Slide 45
#1
#2
Communication
& control
#1
#2
Local control
Communication
& control

## Slide 46
#1
#2
Communication
& control
#1
#3
#2
Local control
Communication

## Slide 47
Do you need to store state?
Are there
multiple
writers?
Can you use
an always
online TTP?
Are all
writers
known?
Are all
writers
trusted?
Is public
verifiability required?
no
no
yes
no
yes
yes
yes
yes
no
no
no
yes
Don’t use
Blockchain
Private
Permissioned
Blockchain
Public
Permissioned
Blockchain
Permissionless
Blockchain
Local energy communities
TTP = Trusted Third party

## Slide 48: Individualist versus collaborative ?

## Slide 49
0
1
2
3
4
5
6
7
8
9
10
20
30
40
50
60
70
80
Battery capacity per household [kWh]
Self-sufficiency [%]
Theoretical limit
Self-sufficiency for daily time intervals
Self-sufficiency for 15 min intervals
Coalition
Individuals
100% equipped
Individuals
50% equipped
storage 2x larger

## Slide 50
A general objective / concepts
  Historical context (not so much an innovation)
  System complexity determining coordination complexity
  Interdependent layers (technical but also economic dispatch and governance),
  Cost allocation has some degrees of freedom with regard to physical flux.
A review of coordination strategies
  Centralized / Decentralized
  Individualist / Collaboration
Our strategy
  Overview
  Order book format
  Central dispatch
    Modularité vue graphiquement ?
    Comparaison avec Alg. 1
    Scalability du nombre de batteries
  Forecast
    Simple, auto-regressor, weather regressor
  Adjustment
    2D of piece-wise and tree view
    Convergence

## Slide 51
May 28
May 29
May 30
May 31
Jun 1
Jun 2
Jun 3
Jun 4
0
10
20
30
40
50
60
Power [kW]
Solar production
Load profile

## Slide 52
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
0.16
0
50
100
150
200
Network fees [€/kWh]
Cost of electricity [€]
17.4 cent€/kWh
3.71 cent€/kWh
No storage
Theoretical limit
Individual strategy
Optimal collaboration

## Slide 53
Central dispatch (scalability)
# of batteries
Optimization time

## Slide 54
Forecast (bare bone, autoregressive, weather)
Time
Power profile
Reference

## Slide 55: Chapter 4

## Slide 56
What's the impact of frequent forecast and redispatch?
Including stochastic variables in the dispatch
Relying on an heuristic strategy without forecast

## Slide 57: Chapter 5 More solar panels is always better for GHG emissions ?

## Slide 58
Self-sufficiency is desirable ?
High self-sufficiency is not desirable, but the right self-sufficiency is (we believe).
Our work is to find the "right level" from an GHG perspective.
Self-sufficiency is interesting to merge :
efficiency gains from large power plants,
and energy sufficiency from a more “physical understanding of production”.

## Slide 59
Pour atteindre une autoproduction de X%, quelle est la combinaison de panneaux solaires et batteries qui minimise l’émission de Gaz à Effet de Serre (GES) ?
les GES à la fabrication et
au démantèlement (l’investissement)
les GES dans la consommation (l’opération)
+
Émissions de GES
=
Notes: L’énoncé du problème
2 composantes pour calculer les émissions (l’une sans l’autre n’a pas de sens)

## Slide 60
Producteurs
Consommateurs
Hypothèse d’une étude à l’échelle de la communauté
0 gCO2/kWh
60 gCO2/kWh
-0 gCO2/kWh
Production
locale
Import du
réseau
- 60 gCO2/kWh
Notes: 1) On a fait un choix, une hypothèse forte
2) Évite les solutions qui consistent à surdimmenssioner le PV pour sa rentabilité carbone à l’export
(éviter de tomber dans une situation où on installe du PV en vu d’un impact National, reste à l’échelle locale).
It is a conservative assumption. We justify this scope with a least three reasons 1) exporting power has technical implications that are not carbon neutral (see Rémy's comment) 2) the philosophy of self-sufficient communities aim at calculating GHG emission at the scale of the community, and not to dilute it at the scale of a country 3) if all energy communities take the assumption of an “infinite” grid is not a sustainable solution system wide.

## Slide 61
Pour atteindre une autoproduction de X%, quelle est la combinaison de panneaux solaires et batteries qui minimise les émissions GES ?
GES gCO2/kWh
Autoproduction
Réseau électrique
60 gCO2/kWh
100%
0%
30%
Notes: Intuiter le résultat (expliquer les axes)
Autoproduction bénéfique pour les aspects émission de gaz à effet de serre
Autoproduction dans l’excès (disproportion des équipements) qui amène à quantativement empirer les émissions

## Slide 62
0
20
40
60
80
0
100
200
300
400
500
Autoproduction [%]
GES [gCO​2​eq / kWh]
1%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Les cas de l’Allemagne
Réseau électrique
Communauté qui consomme la nuit
Communauté qui consomme le jour
Notes: Même graphique à cela qu’on le présente sous forme d’abaque pour différent types de communautés
Intuition validé, coude vers 70% autoproduction (en fait assez « loin »)

## Slide 63
0
20
40
60
80
40
60
80
100
120
140
160
180
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Les cas de la France
Autoproduction [%]
GES [gCO​2​eq / kWh]
Réseau électrique
Notes: Même graphique, mais on commence à un niveau plus bas, grâce au réseau français plus vertueux
Intuition toujours présente, mais cette fois ci moins marqué, coude 20% autoproduction (assez facilement atteint)
De ce point de vue (sous entendu avec nos hypothèses), l’autoconsommation collective n’est pas une solution magique pour réduire nos émissions par kWh
À la fois c’est dommage, mais aussi tant mieux (presque) --> souligne qu’on ne peut pas prendre la solution de la facilité (le kWh à 0gCO2), on échappe aux questions d’usages et de rapport à l’énergie. Pas seulement un question quantitative de sobriété. Rapport à la machine à travers la réparation (ami). Rapport à l’échelle spatio-temporelles réorganisation autour du vélo/transport en commun versus voiture(l’échelle couvre beaucoup de sujet, exemple de la démocratie athénienne à 10 000 âmes pas la même échelle que la démocratie à l’échelle de 66 millions, pourtant ce sont les mêmes mots utilisés).

## Slide 64: Annex 1 City radius ?

## Slide 65
Today electric transport (90km/h) and refrigeration ⇒ Food can be produced anywhere in Europe and brought to cities. Take assumption that this is not available (obviously not realistic). The objective is :
Show without using energy physical limits are more apparent
Calculate a theoretical city size and compare it with pre-industrial cities (validate order of magnitude)
Compare order of magnitude for a city to current megapole
Method
We take a circular city with a radious k, to feed this city we need a circular farming area around with radius r, Finally we have a maximal radius R which considers how far food produce can travel. This is figure X.
Fig X.
The city radius and density of population are variables of our problem. For the rest the « farming » circle is defined by the consumption per inhabitant and crop yield per surface. The « travelling » circle is defined by the horse speed carrying food and duration of the trip (food peremption or other logistic matters).
We express the equation to find the radius of the farming circle as a function of the city radius and population density.
Eq X.

## Slide 66
Results
To calculate the farming circle depends on surface to feed a human, we take this value from WHO. The upper traveling circle is more flexible but for now we set the limit based on horse speed and 3 day trip.
Fig 2 with different assumptions on population density (reading the curve)
Xaxis = city radius & Yaxis = farming circle
Fig 3 Placing pre-industrial big cities / modern small cities / big metropoles (Paris, Tokyo)
Xaxis = city radius & Yaxis = farming circle
Are we good on the validation side ?
Warning not realistic, order of magnitude nonetheless between small cities and big cities ?
Limits
Always careful when using over-simplified models. Rather here to show some trends, highlight potenital physical limits with less energy.
Surface farming per habitant ?
Some food don’t have peremption date, or can be transported alive.
Topology (mountain, river, sea side, circular city)
Train tracks

## Slide 67: Archives / backup slides Random stuffs

## Slide 68
(Society & Energy)
1760 – 1840: Industrial revolution
City:
Taux d’urbanisation / Taille des villes / Matériaux employés à la construction
Work:
70 – 80% of the population employed in agriculture until 1800 [1] against 1.5% in France nowadays.
1865: Abolition of slavery in the USA
Family:
Dispersion of family members: long distance mobility increases continuously during the 19th century [2].
[1] GRIGG, “The World’s Agricultural Labour Force 1800-1970”.
[2] Bourdieu et al., ‘La dispersion spatiale des familles’.

## Slide 69
Individual self-consumption
« Less complex » system:
(see Alg. 1)
Collective self-consumption
« More complex » system:
Maximize
revenues
Multiple
storages
Multiple dwellings
[1] Siegenfeld and Bar-Yam, ‘An Introduction to Complex Systems Science and Its Applications’.
Maximize
revenues
Multiple
storages
A dwelling
Notes: Adding a new scale keep equal or raise the overall complexity (# actions) that the system should consider. From a coherent system to a corralated system (explain).
Research field starts with recognizing this complex systems, and providing coordination designs for it (that exceed the complexity of decision makers within them).
Other complexities aside from the multi actors (revenues – time, distribution grid – localisation)
Complexity provides more action (manage common resources) but does not garantee to perform better (use alg. 1 has a lower bound) to see if we take good decision / the decision space is large enough (if exchange are too expensive…)

## Slide 70
What is the expected complexity of local energy communities (at each scale)?
[1] Siegenfeld and Bar-Yam, ‘An Introduction to Complex Systems Science and Its Applications’.
Coordination actions to maximize revenues
Community #1
« less complex »
Community #2
« more complex »
« Individual » actions
« Exchange » actions
« Temporal » actions
« Spatial » actions
…
« Individual » actions
Grid
Grid
DSO
Boucle sur la communauté
Chiffre entre action
Notes: More or less complex energy communities (with different scales involved, coherent or corrolated)
Coordination with more actions can be necessary but never sufficient for better performance (good action)
Unforeseen evolution of communities, how to design an evolutionary coordination (keep good mutations)?

## Slide 71
System #1
« less complex »
System #2
« more complex »
Multiple batteries
Maximize revenues
Individual houses
⇒ « Individual » actions
Multiple batteries
Maximize revenues
Multiple houses
⇒ « Individual » actions
⇒ « Exchange » actions
⇒ « Temporal » actions
⇒ « Spatial » actions
…
Complexity of the system
at each scale
Complexity of the coordination at each scale
Notes: Before thinking about the coordination strategy, we have to think about the expected complexity of our local energy community at each scale (house, community, DSO, TSO)
  Illustrate examples, complexity of system 1, versus system 2
The complexity at each scale of our system will give us the complexity of coordination we need
  It is necessary for our coordination to have at least the complexity of the system at a given scale (lower bound)
  It is not sufficient as:
    More available actions (complex coordination) do not guarantee a better performance (no because we still need to make good decisions, yes because we can manage exchanges). Individual case actually provide an interesting lower bound on our performance.
    More action can be overwhelming/useless, some actions (degree of freedom) can potentially be eliminated (distribution grid is robust enough, exchange cost are prohibitive)
Accepting that a complex system (community) will present elements that were not considered ahead of time. Thus the question becomes : how to account for an evolutionary process of our coordination strategy (keeping the ”good mutation” and not the bad) ?

## Slide 72
Notes: See reasons to create a community from chapter 1
From a technico-economic perspective, hope to validate equation (which is not the case in France).

## Slide 73
Power [kW]
Morning
Noon
Evening
Surplus
Grid consumption
Local consumption
Consumption
Production
Increase self-sufficiency
Increase revenues (time-of-use, grid services, …)
Lower GHG emissions
Objectives:
Means:
Storage
Shapeable load
Deferable load
Nudges (human)