## Slide 1: Chapter 1 Introduction: Local energy communities ?

## Slide 2: Why local energy communities (in our opinion) ?

## Slide 3
To be consistent with the energy transition: sufficiency, efficiency, renewables [1-4].
Yes but not only.
Renewables: e.g., solar panels
Efficiency: e.g., building insulation
Sufficiency: e.g., lower thermostat
[1] “RTE : Futurs énergétiques 2050”
[2] “ADEME : Transition(s) 2050”
[3] “Shift Project : le plan de transformation de l'économie française”
[4] “NégaWatt : Scénario 2022”
Proximité retrouvée
Trade-off ?
Leopold Kohr, Ivan Illich, Gilbert Simondon, Bruno Latour.

## Slide 4: What are local energy communities (in our opinion) ?

## Slide 5
Energy communities is a flexible concept [1] — i.e., our definition not absolute.
Two ingredients: geographic scope & temporal scope.
“A governance with the participation and effective control of local members whose primary economic activity is not the energy sector,
A primary purpose aimed at generating social and environmental benefits rather than a focus on financial profits.” [2]
[1] Brummer, ‘Community Energy – Benefits and Barriers’.
[2] Lowitzsch, Hoicka, and van Tulder, ‘Renewable Energy Communities under the 2019 European Clean Energy Package – Governance Model for the Energy Clusters of the Future?’

## Slide 6
[1] Jarra Hicks and Nicola Ison. « An Exploration of the Boundaries of ‘Community’ in Community Renewable Energy Projects: Navigating between Motivations and Context ». In: Energy Policy 113 (Feb. 2018), pp. 523–534. doi: 10.1016/j.enpol.2017.10.031

## Slide 7
Power [kW]
Morning
Noon
Evening
Surplus
Grid consumption
Local consumption
Consumption
Production
Self-consumption (see chapter 2):

## Slide 8
In France:
Producers
Consumers
Organizing Legal Entity
Billing
Metering data
Sharing « keys »
Distribution System Operator
Energy
supplier
1 km radius
Electrical grid
…
…
…
30 minutes
1 km radius
Sharing keys:
Static
Dynamic default
Dynamic
Notes: Objet social (communauté d’hommes et de femmes)
On utilise le réseau d’électricité publique (pas d’autarcie)
Chaque consommateur garde un fournisseur extérieur pour couvrir le complément d’électricité
Notion de prise de décision collective sur la répartition du productible.
Couche physique et couche contractuelle

## Slide 9
In August 2021, the regulated price of electricity is 9.74 cent€/kWh before taxes [16], and includes 3.71 cent€/kWh for network fees (TURPE) which means that producers can expect to sell electricity at about 6 cent€/kWh.
With the 2022 regulated price, and if we remove 3.71 cent€/kWh for grid fees, this leaves a potential value of 10 cent€/kWh for producers selling within a community,
If consumers are willing to accept a larger TURPE in the winter, solar power could be sold at about 13 cent€/kWh with a 0.73 cent€/kWh TURPE and still fall below the regulated electricity price.
[PV + battery LCOE] This would enable a price of electricity at 20 cent€/kWh plus 3.71 cent€/kWh and 3.2 cent€/kWh in TURPE and local taxes and a 20 % VAT for a total cost after tax of 32.3 cent€/kWh.
Whether local energy communities can extend on the public grid or not, is a major difference between national implementations in Europe.

## Slide 10: Research landscape and questions.

## Slide 11
Research question #1:
How to coordinate local consumption with production within a community?

## Slide 12
Research question #2:
Is more renewable energy systems always better for local energy communities?

## Slide 13: Chapter 2 What does it means to “self-consume” ?

## Slide 14
Distribution grid
Meter #1
Meter #2
Demand
Production
Feed-in-tariff
Distribution grid
Meter #1
Demand
Production
Self-consumption
Notes: Différence physique limité (compteurs)
Différence économique et « philosophique » marquées

## Slide 15
Power [kW]
Morning
Noon
Evening
Surplus
Grid consumption
Local consumption
Consumption
Production
Self-consumption =
+
Self-sufficiency =
+

## Slide 16: What’s the impact of time intervals ?

## Slide 17
With 30 min intervals:
self-sufficiency = 100%
10 AM
10:30 AM
With 15 min intervals:
self-sufficiency = 50%
…
…
load(t)
prod(t)

## Slide 18
00:00
Jun 1, 2014
12:00
00:00
Jun 2, 2014
12:00
00:00
Jun 3, 2014
12:00
00:00
Jun 4, 2014
0
1
2
3
4
5
6
Power [kW]
Solar production
Load profile

## Slide 19
0
1
2
3
4
5
0
10
20
30
40
50
60
70
80
90
PV size per household [kWp]
Self-sufficiency [%]
5 min
15 min
30 min
60 min
1 day
1 week
1 month
1 year
Diurnal
value gap
(31%)
Seasonal
value gap
(26%)
Weekly
value gap
(5%)

## Slide 20: How to include storage ?

## Slide 21
00:00
06:00
12:00
18:00
-2
-1
0
1
2
3
00:00
06:00
12:00
18:00
-1
0
1
2
3
4
Power [kW]
+
a) Storage = production
00:00
06:00
12:00
18:00
-1
0
1
2
3
4
00:00
06:00
12:00
18:00
-1
0
1
2
3
4
b) Storage = production & demand
Power [kW]
Storage
Production
Consumption
Self-sufficiency
Self-sufficiency
Notes: Storage = demand
SS = 12 / 21 = 57%

## Slide 22
00:00
Jun 2, 2014
03:00
06:00
09:00
12:00
15:00
18:00
21:00
−3
−2
−1
0
1
2
3
4
5
Household power [kW]
−10
−5
0
5
10
15
20
25
30
35
40
45
Self-sufficiency [%]
Metrics
Battery profile
Solar production
Load profile
No storage
Definition 2
Definition 1

## Slide 23
00:00
Jun 2, 2014
03:00
06:00
09:00
12:00
15:00
18:00
21:00
0
1
2
3
4
5
Household power [kW]
0
0.5
1
1.5
2
2.5
0
10
20
30
40
50
60
70
80
PV size [kWp]
Self-sufficiency [%]
Battery profile
Solar production
Load profile
(35%) Definition 2
(33%) Net-metering
(31%) Definition 1

## Slide 24: Do we need storage to “self-consume” ?

## Slide 25
00:00
May 1, 2019
12:00
00:00
May 2, 2019
12:00
00:00
May 3, 2019
12:00
00:00
May 4, 2019
12:00
00:00
May 5, 2019
0
10
20
30
40
50
60
Power [kW]
Solar production
Load profile

## Slide 26
00:00
May 1, 2019
06:00
12:00
18:00
00:00
May 2, 2019
06:00
12:00
18:00
00:00
May 3, 2019
−20
−10
0
10
20
30
40
50
60
Power [kW] — SOC [kWh]
Solar production
Load profile
Battery power profile
Battery SOC

## Slide 27
0
1
2
3
4
5
0
10
20
30
40
50
60
70
80
90
100
PV size [kWp/household]
Self-sufficiency [%]
2 kWh
4 kWh
6 kWh
8 kWh
No storage
1 day
1 year
B
C
A
1.5
10%
10%

## Slide 28: Can a few weeks represent a whole year?

## Slide 29
2
4
6
8
10
12
14
16
18
20
22
24
26
28
30
32
34
36
38
40
42
44
46
48
50
52
0
1
2
3
4
5
6
Number of clusters
Mean Absolute Percentage Error [%]
Score for
Adjusted weeks
[1, 5] kWp
[0, 10] kWh
Score for
actual weeks
Score for
adjusted weeks
K = 5 weeks

## Slide 30
0
10
20
30
40
50
60
70
80
90
100
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Solar panel sizes [kWp]
Self-sufficiency [%]
b = 30 kWh
b = 10 kWh
b = 4 kWh
b = 2 kWh
b = 0 kWh
Whole data-set, i.e., 52 weeks
Clustered data K = 5 weeks

## Slide 31: What is the impact of load on self-sufficiency ?

## Slide 32
0
1
2
3
4
5
0
10
20
30
40
50
60
70
80
90
100
PV size [kWp/household]
Self-sufficiency [%]
Self-consumption
Self-sufficiency
Natural self-sufficiency = 35%
1 year

## Slide 33
00:00
Jun 11, 2019
03:00
06:00
09:00
12:00
15:00
18:00
21:00
0
5
10
15
20
25
30
35
Power [kW]
Solar production
10% NSS
90% NSS
42% NSS

## Slide 34
0.5
1
1.5
2
2.5
3
3.5
4
4.5
0
10
20
30
40
50
60
70
80
90
100
PV size [kWp/household]
Self-sufficiency [%]
1 year
10% NSS
20% NSS
30% NSS
40% NSS
50% NSS
60% NSS
70% NSS
80% NSS
90% NSS
Original data
NSS = 35.5%

## Slide 35: Chapter 3 How to coordinate self-consumption within communities? Part I
Notes: Historical narrative (see ”quoi de neuf” avoid the innovative narrative)
What level of complexity do we expect our communities ?
Not just a question of physical coordination

## Slide 36: What do we mean by coordination?

## Slide 37: What is the expected complexity of local energy communities ?

## Slide 38
What is the expected complexity of local energy communities (at each scale)?
[1] Siegenfeld and Bar-Yam, ‘An Introduction to Complex Systems Science and Its Applications’.
Coordination actions to maximize revenues
Community #1
« less complex »
Community #2
« more complex »
« Individual » actions
« Collective » actions
« Temporal » actions
« Spatial » actions
…
« Individual » actions
Grid
Grid
DSO
1
1
1
1
2, 3, 4
Notes: More or less complex energy communities (with different scales involved, coherent or corrolated)
Coordination with more actions can be necessary but never sufficient for better performance (good action)
Unforeseen evolution of communities, how to design an evolutionary coordination (keep good mutations)?

## Slide 39: What “eco-system” around coordination strategies ?

## Slide 40
Physical
coordination
Social coordination
(governance)
Economical coordination
Defining fairness
Revenues
Selecting
a methodology
Environment
(regulatory, physical)
[1] Mengelkamp et al., ‘Designing Microgrid Energy Markets’.
[2] Cox, Arnold, and Villamayor Tomás, ‘A Review of Design Principles for Community-Based Natural Resource Management’.
Not only physical coordination.

## Slide 41
Costs allocation has some degrees of freedom with physical flux:
Physically at 12:15 pm
Economically at 12:15 pm
kWh
The price is another adjustment variable.
prod. #1
cons. #3
cons. #2
1
2
3
kWh
1
2
3
Pro rata of total consumption
Prioritization of cons. #2
0.66
1.33
1.0
1.0
2
3
share #2 = 33% of 2kWh
share #3 = 66% of 2kWh
share #2 = 1kWh
share #3 = 2kWh - 1kWh
Production
Consumption
[1] Diva et al., ‘’.
Notes: Not only is possible to do without (expected from passive communities)
The economical dispatch has some degree of freedom with regard to physical flux
Physically use all resources « together » and still economically « reward » resource owners (increase the cake size, and still share it how we want).

## Slide 42
Prod. 1
1 | … | 0
… | … | …
0.75 | … | 0.1
Prod. n
…
Cons. 1
Cons. n
…
Time
=100%
=100%
=100%
12:15 pm
12:30 pm
1:00 pm
…
Sharing keys:

## Slide 43: What value for a coalition?

## Slide 44
0
1
2
3
4
5
6
7
8
9
10
20
30
40
50
60
70
80
Battery capacity per household [kWh]
Self-sufficiency [%]
Theoretical limit
Self-sufficiency for daily time intervals
Self-sufficiency for 15 min intervals
Coalition
Individuals
100% equipped
Individuals
50% equipped
storage 2x larger

## Slide 45: A review of coordination strategies
Centralized / Decentralized
Individualist / Collaborative
Notes: Expected complexity we want to reach at each scale (house, community, inter-communities, national)
Physical coordination depends on cost allocation and human organization
Cost allocation can provide a level of abstraction from physical flux (to some extend)
2 axes of review for coordination strategies.

## Slide 46: Decentralized versus centralized ?

## Slide 47
Centralized / Decentralized
[1] Kok and Widergren, ‘A Society of Devices’ (smart energy management matrix).
Notes: ICT = communication (blockchain, virtual machines on a server (agent), central influx, MQTT)
Control = algorithm = ADMM or central optimization or PID, …
Power system = central battery or many small batteries ? Physical distribution of resources
For 3 batteries centralized controller will be more efficient, for 1 million…
Centralized system choosen by a distributed governance ? Is it still distributed ?

## Slide 48
#1
#3
#2
Local control
#1
#2
Local control
Communication

## Slide 49
#1
#2
Communication
& control
#1
#2
Local control
Communication
& control

## Slide 50
#1
#2
Communication
& control
#1
#3
#2
Local control
Communication

## Slide 51
Do you need to store state?
Are there
multiple
writers?
Can you use
an always
online TTP?
Are all
writers
known?
Are all
writers
trusted?
Is public
verifiability required?
no
no
yes
no
yes
yes
yes
yes
no
no
no
yes
Don’t use
Blockchain
Private
Permissioned
Blockchain
Public
Permissioned
Blockchain
Permissionless
Blockchain
Local energy communities
TTP = Trusted Third party

## Slide 52: Individualist versus collaborative ?

## Slide 53: Chapter 4 How to coordinate self-consumption within communities? Part II
Notes: Historical narrative (see ”quoi de neuf” avoid the innovative narrative)
What level of complexity do we expect our communities ?
Not just a question of physical coordination

## Slide 54
May 28
May 29
May 30
May 31
Jun 1
Jun 2
Jun 3
Jun 4
0
10
20
30
40
50
60
Power [kW]
Solar production
Load profile

## Slide 55
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
0.16
0
50
100
150
200
Network fees [€/kWh]
Cost of electricity [€]
17.4 cent€/kWh
3.71 cent€/kWh
No storage
Theoretical limit
Individual strategy
Optimal collaboration

## Slide 56
20
40
60
80
100
0
0.25
0.5
0.75
1
1.25
Number of participants
Time [minutes]
100 households under 75s
Optimization time for 2 days

## Slide 57
20
40
60
80
100
0
2
4
6
8
10
12
14
16
Number of participants
Time [minutes]
14 minutes for 100 households
Optimization time for a full week

## Slide 58
Forecast (bare bone, autoregressive, weather)
Time
Power profile
Reference

## Slide 59
Netload 0.88
Samples: 3360
No
Netload -1.5
Samples: 1540
Yes
…
Netload 2
Samples: 1820
…
…
Linear regression model
No
Yes
No
Yes

## Slide 60
−100
−80
−60
−40
−20
0
20
40
60
80
100
0
5
10
15
20
25
Improvement with linear trees (closer to ) [%]
Occurrence [%]
Median: 35.7%

## Slide 61: Chapter 5

## Slide 62
What's the impact of frequent forecast and redispatch?
Including stochastic variables in the dispatch
Relying on an heuristic strategy without forecast

## Slide 63: Chapter 6 Are more solar panels always better?

## Slide 64
Producers
Consumers
0 gCO2/kWh
60 gCO2/kWh on average
Local power
Grid imports
Local energy community
0 gCO2/kWh
Grid exports
Notes: 1) On a fait un choix, une hypothèse forte
2) Évite les solutions qui consistent à surdimmenssioner le PV pour sa rentabilité carbone à l’export
(éviter de tomber dans une situation où on installe du PV en vu d’un impact National, reste à l’échelle locale).
It is a conservative assumption. We justify this scope with a least three reasons 1) exporting power has technical implications that are not carbon neutral (see Rémy's comment) 2) the philosophy of self-sufficient communities aim at calculating GHG emission at the scale of the community, and not to dilute it at the scale of a country 3) if all energy communities take the assumption of an “infinite” grid is not a sustainable solution system wide.

## Slide 65
GHG emission [gCO2/kWh]
Self-sufficiency
Grid emission: 60 gCO2/kWh
100%
0%
30%
Notes: Intuiter le résultat (expliquer les axes)
Autoproduction bénéfique pour les aspects émission de gaz à effet de serre
Autoproduction dans l’excès (disproportion des équipements) qui amène à quantativement empirer les émissions

## Slide 66
Sep 10
Sep 11
Sep 12
Sep 13
Sep 14
Sep 15
Sep 16
Sep 17
0
100
200
300
400
500
Battery SOC [kWh] & Grid emissions [gCO2/kWh]
2019
Grid emissions
Battery SOC
20% SOC
Grid imports [kW]
Grid exports [kW]
100% SOC

## Slide 67
Aug 6
Aug 7
Aug 8
Aug 9
Aug 10
Aug 11
Aug 12
Aug 13
0
20
40
60
80
100
120
140
2019
Battery SOC [kWh] & Grid emissions [gCO2/kWh]
Grid emissions
Battery SOC
100% SOC
20% SOC
Grid imports [kW]
Grid exports [kW]

## Slide 68
0
10
20
30
40
50
60
70
80
90
100
200
300
400
500
600
700
800
Self-sufficiency [%]
Carbon emission [kgCO​2eq / MWh]
Grid only emission
4.3 kWp/house
10.2 kWh/house
1.7 kWp/house
2.2 kWh/house
20 kWp/house
22 kWh/house

## Slide 69
0
10
20
30
40
50
60
70
80
90
100
50
100
150
200
250
300
350
Self-sufficiency [%]
Carbon emission [kgCO​2eq / MWh]
Grid only emission
1 kWp/house
0 kWh/house
3.1 kWp/house
7.4 kWh/house
7.7 kWp/house
18.1 kWh/house

## Slide 70
0
20
40
60
80
0
100
200
300
400
500
1%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Grid only emission
Natural self-sufficiency
Carbon emission [kgCO​2eq / MWh]
Self-sufficiency [%]
Notes: Même graphique à cela qu’on le présente sous forme d’abaque pour différent types de communautés
Intuition validé, coude vers 70% autoproduction (en fait assez « loin »)

## Slide 71
0
20
40
60
80
40
60
80
100
120
140
160
180
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Carbon emission [kgCO​2eq / MWh]
Self-sufficiency [%]
Grid only emission
Natural self-sufficiency
Notes: Même graphique, mais on commence à un niveau plus bas, grâce au réseau français plus vertueux
Intuition toujours présente, mais cette fois ci moins marqué, coude 20% autoproduction (assez facilement atteint)
De ce point de vue (sous entendu avec nos hypothèses), l’autoconsommation collective n’est pas une solution magique pour réduire nos émissions par kWh
À la fois c’est dommage, mais aussi tant mieux (presque) --> souligne qu’on ne peut pas prendre la solution de la facilité (le kWh à 0gCO2), on échappe aux questions d’usages et de rapport à l’énergie. Pas seulement un question quantitative de sobriété. Rapport à la machine à travers la réparation (ami). Rapport à l’échelle spatio-temporelles réorganisation autour du vélo/transport en commun versus voiture(l’échelle couvre beaucoup de sujet, exemple de la démocratie athénienne à 10 000 âmes pas la même échelle que la démocratie à l’échelle de 66 millions, pourtant ce sont les mêmes mots utilisés).

## Slide 72
0
20
40
60
80
0
100
200
300
400
500
1%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Grid only emission
Natural self-sufficiency
Carbon emission [kgCO​2eq / MWh]
Self-sufficiency [%]
0
20
40
60
80
40
60
80
100
120
140
160
180
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Self-sufficiency [%]
Germany
France
Notes: Même graphique à cela qu’on le présente sous forme d’abaque pour différent types de communautés
Intuition validé, coude vers 70% autoproduction (en fait assez « loin »)

## Slide 73
0
20
40
60
80
0
100
200
300
400
500
Residential community #1
Residential community #2
Residential community #3
University building
Self-sufficiency [%]
1%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
31%
33%
29%
39%
Carbon emission [kgCO​2eq / MWh]
Grid only emission
Natural self-sufficiency

## Slide 74: Chapter 7 Conclusion

## Slide 75: Annex 1 City radius ?

## Slide 76
Today electric transport (90km/h) and refrigeration ⇒ Food can be produced anywhere in Europe and brought to cities. Take assumption that this is not available (obviously not realistic). The objective is :
Show without using energy physical limits are more apparent
Calculate a theoretical city size and compare it with pre-industrial cities (validate order of magnitude)
Compare order of magnitude for a city to current megapole
Method
We take a circular city with a radious k, to feed this city we need a circular farming area around with radius r, Finally we have a maximal radius R which considers how far food produce can travel. This is figure X.
Fig X.
The city radius and density of population are variables of our problem. For the rest the « farming » circle is defined by the consumption per inhabitant and crop yield per surface. The « travelling » circle is defined by the horse speed carrying food and duration of the trip (food peremption or other logistic matters).
We express the equation to find the radius of the farming circle as a function of the city radius and population density.
Eq X.

## Slide 77
Results
To calculate the farming circle depends on surface to feed a human, we take this value from WHO. The upper traveling circle is more flexible but for now we set the limit based on horse speed and 3 day trip.
Fig 2 with different assumptions on population density (reading the curve)
Xaxis = city radius & Yaxis = farming circle
Fig 3 Placing pre-industrial big cities / modern small cities / big metropoles (Paris, Tokyo)
Xaxis = city radius & Yaxis = farming circle
Are we good on the validation side ?
Warning not realistic, order of magnitude nonetheless between small cities and big cities ?
Limits
Always careful when using over-simplified models. Rather here to show some trends, highlight potenital physical limits with less energy.
Surface farming per habitant ?
Some food don’t have peremption date, or can be transported alive.
Topology (mountain, river, sea side, circular city)
Train tracks

## Slide 78: Archives / backup slides Random stuffs

## Slide 79
(Society & Energy)
1760 – 1840: Industrial revolution
City:
Taux d’urbanisation / Taille des villes / Matériaux employés à la construction
Work:
70 – 80% of the population employed in agriculture until 1800 [1] against 1.5% in France nowadays.
1865: Abolition of slavery in the USA
Family:
Dispersion of family members: long distance mobility increases continuously during the 19th century [2].
[1] GRIGG, “The World’s Agricultural Labour Force 1800-1970”.
[2] Bourdieu et al., ‘La dispersion spatiale des familles’.

## Slide 80
Individual self-consumption
« Less complex » system:
(see Alg. 1)
Collective self-consumption
« More complex » system:
Maximize
revenues
Multiple
storages
Multiple dwellings
[1] Siegenfeld and Bar-Yam, ‘An Introduction to Complex Systems Science and Its Applications’.
Maximize
revenues
Multiple
storages
A dwelling
Notes: Adding a new scale keep equal or raise the overall complexity (# actions) that the system should consider. From a coherent system to a corralated system (explain).
Research field starts with recognizing this complex systems, and providing coordination designs for it (that exceed the complexity of decision makers within them).
Other complexities aside from the multi actors (revenues – time, distribution grid – localisation)
Complexity provides more action (manage common resources) but does not garantee to perform better (use alg. 1 has a lower bound) to see if we take good decision / the decision space is large enough (if exchange are too expensive…)

## Slide 81
What is the expected complexity of local energy communities (at each scale)?
[1] Siegenfeld and Bar-Yam, ‘An Introduction to Complex Systems Science and Its Applications’.
Coordination actions to maximize revenues
Community #1
« less complex »
Community #2
« more complex »
« Individual » actions
« Exchange » actions
« Temporal » actions
« Spatial » actions
…
« Individual » actions
Grid
Grid
DSO
Boucle sur la communauté
Chiffre entre action
Notes: More or less complex energy communities (with different scales involved, coherent or corrolated)
Coordination with more actions can be necessary but never sufficient for better performance (good action)
Unforeseen evolution of communities, how to design an evolutionary coordination (keep good mutations)?

## Slide 82
System #1
« less complex »
System #2
« more complex »
Multiple batteries
Maximize revenues
Individual houses
⇒ « Individual » actions
Multiple batteries
Maximize revenues
Multiple houses
⇒ « Individual » actions
⇒ « Exchange » actions
⇒ « Temporal » actions
⇒ « Spatial » actions
…
Complexity of the system
at each scale
Complexity of the coordination at each scale
Notes: Before thinking about the coordination strategy, we have to think about the expected complexity of our local energy community at each scale (house, community, DSO, TSO)
  Illustrate examples, complexity of system 1, versus system 2
The complexity at each scale of our system will give us the complexity of coordination we need
  It is necessary for our coordination to have at least the complexity of the system at a given scale (lower bound)
  It is not sufficient as:
    More available actions (complex coordination) do not guarantee a better performance (no because we still need to make good decisions, yes because we can manage exchanges). Individual case actually provide an interesting lower bound on our performance.
    More action can be overwhelming/useless, some actions (degree of freedom) can potentially be eliminated (distribution grid is robust enough, exchange cost are prohibitive)
Accepting that a complex system (community) will present elements that were not considered ahead of time. Thus the question becomes : how to account for an evolutionary process of our coordination strategy (keeping the ”good mutation” and not the bad) ?

## Slide 83
Notes: See reasons to create a community from chapter 1
From a technico-economic perspective, hope to validate equation (which is not the case in France).

## Slide 84
Power [kW]
Morning
Noon
Evening
Surplus
Grid consumption
Local consumption
Consumption
Production
Increase self-sufficiency
Increase revenues (time-of-use, grid services, …)
Lower GHG emissions
Objectives:
Means:
Storage
Shapeable load
Deferable load
Nudges (human)